## Slide 1
FILM IMAGING
DEPARTMENT OF ORAL MEDICINE AND RADIOLOGY
Dr. Pratima Soni
Senior Lecturer

## Slide 2: CONTENTS
INTRODUCTION
DISCRIPTION OF FILMS
X- RAY FILMS

## Slide 3: INTRODUCTION
A beam of x- ray photons that passes through the dental arches is reduced in intensity by absorption and scattering of photons out the primary beam.
The pattern of the photon that exists the patient, the remnant beam, conveys information about the patients anatomy.
For this information to be useful diagnostically, the remnant beam must be recorded on an image receptor.
The image receptor most often used in dental radiography is X- ray film.

## Slide 4: CONTENTS
INTRODUCTION
INTENSIFYING SCREENS
CASETTES
X- RAY FILMS

## Slide 5: CLASSIFICATION OF X RAY FILMS
BASED ON USE
INTRAORAL
EXTRAORAL
1.PERIAPICAL
2. OCCLUSAL
3. BITE WING

## Slide 6: CLASSIFICATION OF X RAY FILMS
BASED ON SPEED
SLOW SPEED FILMS
FAST SPEED FILMS
HYPERSPEED G FILMS
1. Very small grains of silver bromide
2. Emulsion on one side
3. Better definition
4. Greater Exposure
1. Larger grains of silver bromide
2. Emulsion on both side
1. Can significantly reduce patient exposure
A,B,C Speed
D-ULTRA
E- EKTA
F- ULTRA EKTA

## Slide 7: CLASSIFICATION OF X RAY FILMS
BASED ON USE OR NON USE OF SCREENS
SCREEN FILMS
NON SCREEN FILMS
SENSITIVE TO BLUE LIGHT
SENSITIVE TO GREEN LIGHT

## Slide 8: INTRAORAL FILMS
CLASSIFICATION
SIZES OF INTRAORAL FILMS
DESCRIPTION OF FILMS
CONTENTS
COMPOSITION

## Slide 9: CLASSIFICATION OF INTRAORAL FILMS
BASED ON USE
PERIAPICAL FILMS
BITEWING FILMS
OCCLUSAL FILMS

## Slide 10
SIZES OF IOPA FILMS
22 * 35 mm
24 * 40 mm
30.5 * 40.5 mm
57 * 76 mm

## Slide 11: DESCRIPTION OF INTRAORAL FILMS
TUBE SIDE
LABEL SIDE

## Slide 12: DESCRIPTION OF INTRAORAL FILMS
OUTER PLASTIC WRAPPING
ROUNDED CORNERS
EMBOSSED DOT
2 SIDES
1. TUBE SIDE
2. LABEL SIDE
TUBE SIDE
LABEL SIDE

## Slide 13: CONTENTS OF INTRAORAL FILMS
WATERPROOF OUTER COVER
BLACK PAPER
FILM
WATERPROOF OUTER COVER
LEAD FOIL BACKING
BLACK PAPER

## Slide 14
PURPOSE OF LEAD FOIL
Absorbs X-rays which pass through the film and prevent them from reaching tongue and other structures
Absorbs back scatter radiation and prevents fogging
Secondarily gives stiffness but not rigidity to whole film packet

## Slide 15
WHAT HAPPENS IF THE FILM IS PLACED IN REVERSE
Shadow of the foil is seen on the resultant radiograph
TYRE TRACK or HERRINGBONE APPEARANCE

## Slide 16
PURPOSE OF BLACK PAPER
Protect it form light leak

## Slide 17
COMPOSITION OF THE X RAY FILM
PROTECTIVE LAYER
EMULSION
ADHESIVE LAYER
BASE
EMULSION
ADHESIVE LAYER
PROTECTIVE LAYER

## Slide 18: BASE
Transparent supporting material
on which the emulsion is coated
Polyethylene terephthalate (Polyester)
Thickness = 0.2mm

## Slide 19
PROPERTIES OF THE BASE
Should have proper amount of flexibility to allow ease of handling
Translucent, casting no pattern on the resultant radiograph
Should have a Bluish tint for optimal viewing of the diagnostic detail
Should be able to withstand exposure to processing solutions without distorting, heat, moisture and chemical exposure

## Slide 20: ADHESIVE LAYER
TO ENSURE GOOD ADHESION TO THE SENSITIVE EMULSION LAYER AND THE BASE

## Slide 21
CONSISTS OF
SILVER HALIDE CRYSTALS
1. Silver bromide (80-99%)
2. Silver iodide (1-10%)
3. Mean diameter of silver Halide grain is 0.70 – 0.75 mm
4. Silver halide crystals absorb radiation during X-Ray exposure and store energy from the radiation
5. SILVER IODIDE – Adds greatly to the sensitivity of the film emulsion, thereby reducing the radiation dose required to produce an adequate diagnostic image
GELATIN MATRIX
1. Made from cattle bone and helps to keep the silver grain evenly dispersed.
2. During processing the gelatin absorbs the processing solutions and helps to allow the chemicals to react with the halide grains
EMULSION
Coated on both the sides
Photosensitive to visible light and X-rays
Insight(1.8 um dia)

## Slide 22
PROTECTIVE LAYER
It is a protective, transparent, nonabrasive layer over the emulsion.
An additional layer of Gelatin over the emulsion to serve as a protective barrier
Protects film from damage by mechanical handling, such as scratching, contamination and pressure from rollers during the automatic processing.

## Slide 23: BITEWING FILMS
To record the crowns of Maxillary and Mandibular teeth in one film.
Tab projecting from the middle of the film on which the patient bites to support the film.
Detection of inter-proximal caries
Visualize the alveolar crest and assessment of periodontal disease.

## Slide 24: CLASSIFICATION OF X RAY FILMS
BASED ON USE
INTRAORAL
EXTRAORAL
1.PERIAPICAL
2. OCCLUSAL
3. BITE WING

## Slide 25: EXTRA ORAL FILMS
An extra-oral film is that which is placed outside the mouth during x-ray exposure
Extra-oral films are used to examine large areas of the skull or jaws

## Slide 26: SIZES OF EXTRAORAL FILMS
LATERAL OBLIQUE FILM: 5×7 inches
PANORAMIC FILM: 6×12 inches
CEPHALOMETRIC FILM: 8×10 inches
SKULL RADIOGRAPHY: 10×12 inches

## Slide 27
In extra-oral radiography, screen films are used in combination with two special equipment items:- 1)Intensifying screens 2) Cassettes

## Slide 28: SCREEN FILMS
A screen film is placed between two special intensifying screens in a cassette.
When the cassette is exposed to x-rays, the screens convert the x-ray energy into light, which in turn exposes the screen film.
Screen film is sensitive to fluorescent light rather than direct exposure to x-radiation.
BLUE LIGHT SENSITIVE GREEN LIGHT SENSITIVE

## Slide 29: INTENSIFYING SCREENS
An Intensifying Screen, is a device that transfers x-ray energy into visible light, the visible light, in turn, exposes the screen film. These screens intensify the effect of X-RAYS on the film, thus less radiation is required to expose a screen film, and thus the patient is exposed to less radiation.

## Slide 30
An intensifying screen is a smooth plastic sheet coated with minute fluorescent crystals known as PHOSPHORS.
When exposed to x-rays, the phosphors FLUORESCE and emit visible light in the blue or green spectrum; the emitted light then exposes the film.

## Slide 31: COMPOSITION
BASE-. It is about 0.25mm thick.
The base is the supporting component of the screen.

## Slide 32
Serves to redirect the film a large fraction of the emitted visible light which is moving away from the film.
Thus it increases the sensitivity but some degree of un-sharpness is created because of divergence of light emitted back to the film.
REFLECTING LAYER

## Slide 33
PHOSPHOR LAYER-
Composed of phosphorescent crystals, which absorb x ray photons and fluoresce.
Rare earth intensifying screens using
  terbium-activated gadolinium oxysulphide and
  thelium-activated lanthanum oxybromide,
  fluoresce in the green portion of the spectrum.

## Slide 34
COAT- This layer protects the phosphor layer from mechanical insult such as abrasion, scratching etc.

## Slide 35: CASSETTE
A CASSETTE is a special device that is used to hold the extra-oral film and the intensifying screen.
Cassettes are available in a variety of sizes that correspond to the film and screen sizes.

## Slide 37
IMAGE- PICTURE OR LIKENESS OF AN OBJECT. RECEPTOR- THAT RESPONDS TO A STIMULUS. Images are recorded on the dental x ray film when the film is exposed to a stimulus-specifically energy in the form of X radiation or light.